## Slide 1
10
9
8
7
6
5
4
3
2
1
0

## Slide 2
Robotics Corner

## Slide 3
URDF

## Slide 4
AGENDA
01
02
03
04
URDF components
Writing a simple URDF file
Building your robot urdf
What is URDF
05
Simulation

## Slide 5: URDF in ROS
Make a model of your robot
01285960031
01285960031
www.roboticscorner.tech

## Slide 6
Definition
URDF, Unified Robot Description Format is an XML format for representing a robot model. URDF is commonly used in Robot Operating System tools such as rviz and Gazebo simulator. The model consists of links and joints motion.
01
What is URDF
01285960031
01285960031
www.roboticscorner.tech

## Slide 7
01
What is URDF
01285960031
01285960031
www.roboticscorner.tech
URDF is XML, which is a text format. So you can create the files in any text editor. An IDE with good XML support is recommended.
If there already exists a CAD model of the robot, there are some tools that can be used to convert the CAD model to URDF. Here is a non-exhaustive list:
  PTC Creo to URDF (iCub)
  SolidWorks URDF exporter
  fusion2urdf
  OnShape to Robot
  Phobos Blender plugin

## Slide 8
01
What is URDF
01285960031
01285960031
www.roboticscorner.tech

## Slide 9: What is Gazebo
01
What is URDF
01285960031
01285960031
www.roboticscorner.tech
Gazeboisanopen-source3Droboticssimulator.Physicsengine
3Drendering
Sensorsimulation
IntegrationwithROS

## Slide 10: Let’slaunchsomesimulation(video)
01
What is URDF
01285960031
01285960031
www.roboticscorner.tech
$sudoapt-getinstallros-<distro>-husky-simulator
$source/opt/ros/melodic/setup.bash
$exportHUSKY_GAZEBO_DESCRIPTION=$(rospackfindhusky_gazebo)/urdf/description.gazebo.xacro
$roslaunchhusky_gazebohusky_playpen.launchkinect_enabled:=true
In another terminal to check that the sensors work #activate ROS
$rqt_image_view
Inanotherterminaltocontrol #activateROS
rosrunteleop_twist_keyboardteleop_twist_keyboard.py

## Slide 11: URDF components
02
URDF components
01285960031
01285960031
www.roboticscorner.tech

## Slide 12
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
To define a robot we have to describe all the parts(aka links) and connections between them (aka joints).
Ros and Gazebo take care of geometrical transformations (tf module), Physics simulation and rendering.

## Slide 13: Common joint types in urdf
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
  Fixed: rigid connection
  Revolute: 1D rotation
  Continuous: unlimited revolutions.
  Prismatic: 1D translation
  Planar: 2D translation
  Floating: unlimited 6D
Note: we mostly use the first 4 types
Fixed joint
Continuous joint

## Slide 14: URDF file components
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
Link element
  Visual
  Collision
  Inertial
Joint element

## Slide 15: Link element
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
<link>
<visual>
<geometry>
<cylinder/>
</geometry>
<origin/>
</visual>
<collision>
<geometry>
<cylinder/>
</geometry>
<origin/>
</collision>
<inertial>
<mass>
<origin>
<inertia/>
</inertial>
</link>

## Slide 16: Visual
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
<visual>
<geometry>
<cylinder/>
</geometry>
<origin/>
</visual>
Visual
Joint

## Slide 17: Collision
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
<collision>
<geometry>
<cylinder/>
</geometry>
<origin/>
</collision>
Visual
Joint

## Slide 18: Inertial
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
<inertial>
<mass>
<origin>
<inertia/>
</inertial>
Visual
Joint

## Slide 19: Joint element
02
URDF components
01285960031
01285960031
www.roboticscorner.tech
<joint name="my_joint" type="">
<origin/>
<parent link="link1"/>
<child link="link2"/>
</joint>

## Slide 20: Make a URDF
03
Make a URDF
01285960031
01285960031
www.roboticscorner.tech

## Slide 21: We can make a simple shape first
03
Make a URDF
01285960031
01285960031
www.roboticscorner.tech
First make a urdf folder in the package
  Mkdir urdf
Then make the file:
  Touch oneshape.urdf
Follow the code in this link:
  http://wiki.ros.org/urdf/Tutorials/Building%20a%20Visual%20Robot%20Model%20with%20URDF%20from%20Scratch

## Slide 22: Simple shape urdf:
03
Make a URDF
01285960031
01285960031
www.roboticscorner.tech
<?xml version="1.0"?>
<robot name="myfirst">
<link name="base_link">
<visual>
<geometry>
<cylinder length="0.6" radius="0.2"/>
</geometry>
</visual>
</link>
</robot>

## Slide 23: Add more shapes and joint:
03
Make a URDF
01285960031
01285960031
www.roboticscorner.tech
<robot name="origins">
<link name="base_link">
<visual>
<geometry>
<cylinder length="0.6" radius="0.2"/>
</geometry>
</visual>
</link>
<link name="right_leg">
<visual>
<geometry>
<box size="0.6 0.1 0.2"/>
</geometry>
<origin rpy="0 1.57075 0" xyz="0 0 -0.3"/>
</visual>
</link>
<joint name="base_to_right_leg" type="fixed">
<parent link="base_link"/>
<child link="right_leg"/>
<origin xyz="0 -0.22 0.25"/>
</joint> </robot>

## Slide 24: Building your robot URDF
04
Building your robot urdf
01285960031
01285960031
www.roboticscorner.tech

## Slide 25: This is our robot
04
Building your robot urdf
01285960031
01285960031
www.roboticscorner.tech
It consists of:
  2 wheels in the back
  1 front wheel
  Lidar
  Body
  Electrical components

## Slide 26: Make an environment in gazebo
05
Simulation
01285960031
01285960031
www.roboticscorner.tech

## Slide 27
05
Simulation
01285960031
01285960031
www.roboticscorner.tech

## Slide 28
05
Simulation
01285960031
01285960031
www.roboticscorner.tech

## Slide 29: Adding walls
05
Simulation
01285960031
01285960031
www.roboticscorner.tech

## Slide 30: Add stairs
05
Simulation
01285960031
01285960031
www.roboticscorner.tech

## Slide 31: Add levels
05
Simulation
01285960031
01285960031
www.roboticscorner.tech

## Slide 32: Change colors
05
Simulation
01285960031
01285960031
www.roboticscorner.tech

## Slide 33: Resources for learning
00
Resources
01285960031
01285960031
www.roboticscorner.tech
Tutorialshttp://wiki.ros.org/urdf_tutorial
http://gazebosim.org/tutorials
Learningbycopyingturtlebot3https://emanual.robotis.com/docs/en/platform/turtlebot3/simulation/
huskyhttp://wiki.ros.org/husky_gazebo/Tutorials/Simulating%20Husky
husky+slamhttps://github.com/incebellipipo/carto_demo
Moreadvancedexampleshttps://github.com/AutoRally/autorally
https://mushr.io/tutorials/intro-to-ros/

## Slide 35
Robotics Corner
Robotics Corner
Robotics Corner
Robotics Corner
01211626904
www.roboticscorner.tech