## Slide 1
10
9
8
7
6
5
4
3
2
1
0

## Slide 2
Robotics Corner

## Slide 3
Computer vision with ROS

## Slide 4
AGENDA
01
02
03
04
Installing OpenCV
Bridging OpenCV and ROS
OpenCV Features
OpenCV Overview
05
Coding

## Slide 5: Computer vision and ROS
OpenCV with ROS
01285960031
01285960031
www.roboticscorner.tech
Adapted from Dr. Haitham El-Hussieny, PhD slides

## Slide 6: OpenCV
The most common image processing library is OpencV
01
01285960031
01285960031
www.roboticscorner.tech
OpenCV stands for Open Source Computer Vision Library.
It is a powerful and reliable library for image processing and computer vision tasks.
Free for both academic and commercial use
Available in both python and C++ with functions having different syntax
Windows, MacOS, Linux, iOS, Android
Strong focus on real-time (written in C++ and optimized)
OpenCV Overview

## Slide 7: Computer vision:
01
01285960031
01285960031
www.roboticscorner.tech
OpenCV Overview
Machines see and process everything using numbers, including images and text. How do you convert images to numbers – I can hear you wondering. Two words – pixel values:

## Slide 8
01
OpenCV Features
01285960031
01285960031
www.roboticscorner.tech
Image segmentation
Image Thresholding
Object Detection and Recognition
Edge Detection
Video/Image Input Output.
Shapes Drawing
Changing Color Spaces
OpenCV Features

## Slide 9: Image Thresholding
01
01285960031
01285960031
www.roboticscorner.tech
In digital image processing, thresholding is the simplest method of segmenting images. From a grayscale image, thresholding can be used to create binary images.
OpenCV Features

## Slide 10: Image Segmentation
01
01285960031
01285960031
www.roboticscorner.tech
Image segmentation is the process of partitioning a
digital image into more meaningful and easier to
analyze multiple image segments.
OpenCV Features

## Slide 11: Object Detection and Recognition.
01
01285960031
01285960031
www.roboticscorner.tech
Detection of instances of semantic objects of a certain class (humans, buildings, or cars) in digital images.
OpenCV Features

## Slide 12: Edge Detection.
01
01285960031
01285960031
www.roboticscorner.tech
Edge detection includes a variety of mathematical methods that aim at identifying edges, curves in a digital image at which the image brightness changes sharply or, more formally, has discontinuities.
OpenCV Features

## Slide 13: Video/Image Input Output.
01
01285960031
01285960031
www.roboticscorner.tech
OpenCV loads and saves images and videos from the disk or from a USB cams.
OpenCV Features

## Slide 14: Shapes Drawing.
01
01285960031
01285960031
www.roboticscorner.tech
OpenCV can be used to draw basic shapes on images or videos.
OpenCV Features

## Slide 15: Installing OpenCV.
01285960031
01285960031
www.roboticscorner.tech

## Slide 16: On ROS Noetic.
02
01285960031
01285960031
www.roboticscorner.tech
sudo apt-get update
$ sudo apt-get install ros-noetic-vision-opencv
In case you face a problem with imshow,
$ sudo apt-get install libopencv-*
$ pip install opencv-c
Install usb-cam:
$ sudo apt-get install ros-noetic-usb-cam
Install image-view:
$ sudo apt-get install ros-noetic-image-view
Installing OpenCV

## Slide 17: Bridging OpenCV and ROS
01285960031
01285960031
www.roboticscorner.tech

## Slide 18
03
01285960031
01285960031
www.roboticscorner.tech
The challenge is the image type
supported by ROS is different from the
one that is supported by OpenCV.
CvBridge allows to convert from ROS to
OpenCV format and vice versa.
Bridging OpenCV and ROS

## Slide 19: Implementation
01285960031
01285960031
www.roboticscorner.tech

## Slide 20: Make package and files
04
01285960031
01285960031
www.roboticscorner.tech
1. Create a new ROS package:
  $ cd catkin ws/src/
  $ catkin create pkg my image processing std msgs rospy roscpp sensor msgs image transport cv bridge
2. catkin make in your workspace:
  ~/catkin_ws/$ catkin make
3. create a new python script in the script folder:
  ~/catkin_ws/src/my image processing/scripts/$ gedit image processing.py
Implementation

## Slide 21: Write the image subscriber code
04
01285960031
01285960031
www.roboticscorner.tech
4. Write the image subscriber code:
Import important libraries and create a bridge object
  import rospy
  import cv2
  from std msgs.msg import String
  from sensor msgs.msg import Image
  from cv bridge import CvBridge, CvBridgeError
  import sys
  bridge = CvBridge() #Create a bridge
Implementation

## Slide 22: main function
04
01285960031
01285960031
www.roboticscorner.tech
  def main(args):
    rospy.init node ( ’image converter’, anonymous=True)
    image sub = rospy.Subscriber(”/usb cam/image raw”, Image, image callback)
      try :
      rospy.spin()
      except KeyboardInterrupt:
      print ( ”Shutting down”)
      cv2.destroyAllWindows()
  If __name__ == ’__main__ ’ :
  main(sys.argv)
Implementation

## Slide 23: receiving image callback
04
01285960031
01285960031
www.roboticscorner.tech
def image callback(ros image):
  print ( ’got an image’)
  global bridge
  try :
  cv image = bridge.imgmsg to cv2(ros image, ’bgr8’)
  except CvBridgeError as e:
    print (e)
    #from now you can work with opencv commands:
    cv2.imshow(”Image window”, cv image)
    cv2.waitKey(3)
Implementation

## Slide 24
04
01285960031
01285960031
www.roboticscorner.tech
5. Make sure the libraries are define im CMakeLists.txt:
6. change the python file to executable:
$ chmod a+x scripts/image processing.py
Implementation

## Slide 25
04
01285960031
01285960031
www.roboticscorner.tech
7. catkin make your ROS workspace.
  $ catkin_make
8. Run the image processing.py node:
  $ roscore
  $ rosrun my_image_processing image_processing.py
9. Run the usb cam node:
  $ rosrun usb_cam usb_cam_node __pixel_format:=yuyv
10. Verify the image topic is published by rostopic list.
  $ rostopic list
Implementation

## Slide 26: ADDING A PUBLISHER TO SHOW IMAGE WITH EDGES.
04
01285960031
01285960031
www.roboticscorner.tech
  def main(args):
  rospy.init node ( “image_converter”, anonymous=True)
  Image_sub = rospy.Subscriber(“/usb_cam/image_raw”, Image, image_callback)
  global image_pub
  Image_pub = rospy.Publisher(“/canny_image”,Image)
#from now you can work with opencv commands:
  cv2.imshow(“Building your robot urdf
  Image_window”, cv image)
  cv2.waitKey(3)
  Edge_image = cv2.Canny(cv_image,100,200)
  Ros_image = bridge.cv2_to_imgmsg(edge_image)
  Image_pub.publish(ros_image)
Implementation

## Slide 27: If you are facing any problems in the code try replacing the “ double quotes” and the underscores
04
01285960031
01285960031
www.roboticscorner.tech
Implementation

## Slide 29
Robotics Corner
Robotics Corner
Robotics Corner
Robotics Corner
01211626904
www.roboticscorner.tech